## Slide 1
Soft Jamming Robotic Gripper
An alternative approach to a compliant .hand
Douglas Tilley & Liam Grazier

## Slide 2: Why a hybrid?
In modern robotics, generally 3 different types of gripper are found, these are solid grippers, soft grippers and hybrid grippers.
A brief comparison
Solid Grippers
Pros
Cheap
Robust, tried design
Predictable Behaviour
Cons
No Compliance
Simple
Requires a lot of human programming and path planning
Designed specifically for one job
Hybrid Grippers
Pros
Often designed for multiple jobs
Efficient
Carry some compliance
Predictable Behaviour
Cons
Research based designs currently
Expensive
Can be unique/untested
Soft Grippers
Pros
Compliant behaviour
Cons
Research based designs currently
Difficult manufacturing process
Can often be unpredictable
The point of the hybrid design of gripper is to take the compliance of a Soft robotic gripper and to combine it with the predictable behaviour of the solid gripper.
This allows for a wider range of tasks to be performed.

## Slide 3
Project Progress:
Task | 30/09/2018 | 07/10/2018 | 14/10/2018 | 21/10/2018 | 28/10/2018 | 04/11/2018 | 11/11/2018 | 18/11/2018 | 25/11/2018 | 02/12/2018 | 09/12/2018 | 11/12/2018
Initial Project Design |  |  |  |  |  |  |  |  |  |  |  | 
Preliminary Prototype of Digit |  |  |  |  |  |  |  |  |  |  |  | 
Materials Research and Eval |  |  |  |  |  |  |  |  |  |  |  | 
Motor Research and Requisition |  |  |  |  |  |  |  |  |  |  |  | 
Electronics Development |  |  |  |  |  |  |  |  |  |  |  | 
Rapid Prototyping + Development |  |  |  |  |  |  |  |  |  |  |  | 
Final Build + Intergration of all systems |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 4: Design key structure
The hybrid gripper is broken down into 5 main parts:-
Finger
Base
Jamming principle
  Air vs Water
  Filter type
  Outer material
Electronics
Code
Each of these sections had their own design development

## Slide 5
Design progression
Over the course of this project the design has changed in various ways due to limitations and improvements found.
The rapid prototyping focus of this project meant that each part was developed and improved multiple times with the number of design iterations listed below:
Finger – 7 iterations
  Starting out as a simple square and no additional features.
  Added and moved the height of the tendon holes.
  Posts on the back of the finger were added to give an elasticated limit.
  The posts couldn’t deal with the forces exerted when 3D printed and hence were thickened.
Bases – 3 iterations
  Started out as a fixed square intending to be a hand formation.
  This was quickly changed to a 3 pronged design.
  Had to change the base design due to motor design change.
  The base was made larger and features removed for simplicity.
Pneumatic Rack – 1 iteration
Spindles – 2 iterations
  Initially designed for a specific motor
  Had to be adapted due to technical challenges
CAD Preview of the different iterations of designing the finger parts

## Slide 6
Electronic Developments:
Had issues controlling motors.
Started developing low power stepper motor solution.
Multiple Stepper Motor Controller developed for six motors.
Three for tendon control.
Three for crushing control.
Issue found using 28BYJ-28 stepper motors. Not powerful enough for either task, switched out for NEMA17 Stepper motors .
Electronic progression
The basis of this project was around the motors that had to be used. They had 2 tasks and each required 3 motors. This was the individual finger control and individual finger pneumatic control.
Due to various issues encountered during programming, the project changed motors 3 times.
Robotis Dynamixel MX-28
Originally this motor was intended to be used, however the motors were unresponsive to programming and hence had to be swapped out for a different stepper.
28BYJ-48 5V DC Stepper Motor
These were the second motors looked at for use in this project, using ULN2003 Chips to control the stepper motor.
However the stall torque of the motors was too low and hence couldn’t be used.
Nema17
Nema17s carry industry weight as being reliable and easy to program whilst having a reasonable stall torque.

## Slide 7
Necessary changes
Currently each finger can be position controlled, however it is a rough working with some flaws.
The air system is not sealed correctly, however the principle works(See table). Hence the pneumatics need an overhaul.
Friction of the syringe limits its ability due to torque issues with motors.
Design needs to be optimized still.
Aims, Achievements and Future development
Aims
Individual finger control
Pneumatic Control
Ability to grip
Achievements
Individual Finger Control
Automatic Rack and Pinion Control
Some ability to grip
Future Developments
Improve the interfacing between digit and base
Make the pneumatics air tight
Reduce sizes.
Project Development
Conclusion
The Soft jamming robotic gripper, when fully functional will provide added gripping ability to a traditional gripper, however getting to the stage where this works is difficult.

## Slide 8: Some references for now
https://www.pneumatictips.com/going-soft-on-grippers/
https://www.sciencedirect.com/science/article/pii/S1877050911006958
https://jfi.uchicago.edu/~jaeger/group/JaegerGroupPapers/granular/TRO2171093.pdf
https://www.pnas.org/content/107/44/18809